Radiation Shielding

Alpha, beta, gamma, and X-rays can pass through matter, but can also be absorbed or scattered in varying degrees depending on the material and on the type and energy of the radiation. Medical X-ray images are possible because bones absorb X-rays more so than do soft tissues. Strongly radioactive sources are often stored in heavy lead boxes to shield the local environment from the radiation.

Some materials absorb beta rays. A sheet of common Aluminum will absorb some of the betas, but will allow most to pass through. You can measure this absorption by fixing a beta source and a radiation monitor so their positions do not change, and then inserting layers of Aluminum between them.

When an absorber is in the path of beta rays, it will allow a certain fraction f to pass through. The fraction f depends on the density and thickness of the absorber, but will be a constant for identical absorbers and fixed beta ray energy. If the number of counts detected in a count interval is N0 when no absorber is in place, then the counts N with the absorber is N = f N0. In the preliminary questions, you will develop a more general expression for additional layers of Aluminum absorbers, and then test it against real data.

In this experiment you will use a small source of beta radiation. Beta rays are high-energy electrons. Follow all local procedures for handling radioactive materials.

objectives

- Create a model for the absorption of radiation by matter.

- Use a radiation counter to study how the radiation emitted by a beta source is absorbed by Aluminum.

- Test the model against experimental data to determine its validity

- Calculate the decay energy for Sr-90 beta decay.

Materials

| Power Macintosh or Windows PC LabPro or Universal Lab Interface | Vernier Radiation Monitor or Student Radiation Monitor |
| --- | --- |
| Logger Pro Ten 5-in ( 7-in identical Aluminum squares 0.02678 cm thick | Strontium-90 0.1C source taped to small support adhesive tape |

preliminary Procedure and questions

- Place your Sr-90 source on a table. Turn on the radiation monitor to the audio mode, so that it beeps when radiation is detected. By holding the monitor near the source, determine the most sensitive place on the detector.

- Attach the source disc to a support using a ring stand and a test tube holder so that the source held above the center of the Geiger tube in the radiation monitor. Do not cover the source with tape. Place the source so it is about four centimeters from the most sensitive place on the monitor, so that there is room to place all ten layers of aluminum between the source and the monitor. It is essential that neither the source nor the monitor move during data collection. 

With only air between the source and the monitor, listen to the beep rate for a short while. Now place five layers of aluminum between the source and the monitor, taking care not to move either one. Listen again, and determine if the beep rate is larger, smaller, or unchanged. Now add five more layers of aluminum, again not moving the source or monitor. Listen, and determine the change of the beep rate, if any. Does the aluminum seem to shield the monitor from the beta radiation?

- Based on your observations, sketch a qualitative graph of the beep rate vs. number of layers of shielding.

- In the introduction we used the expression N = f N0 to describe the transmission of betas by one layer of aluminum. Assuming this model, how many counts would be detected if you added a second layer of aluminum, identical to the first, which also transmitted a fraction f? For example, if the first layer transmitted 90% of the radiation, then the second would transmit 90% of that transmitted by the first. The overall transmission would then be 0.90 ( 0.90 = 0.81 = 81% of the no-shielding number of counts. In the data table, write a general expression for the number of counts N detected for any number x of identical layers, each of which transmits a fraction f of the incident radiation. Use N0 as the counts detected when no shielding layers are used. You have just developed a model for the transmission of radiation through matter. Next you will test your model against experimental data.

- Is your model consistent with your qualitative graph you sketched based on initial observations? Remember than f is a number less than one. Add the model function to your sketch without worrying about the vertical scale.

Procedure

- Connect the radiation monitor to SONIC/DIG 1 of the LabPro or to DG 1 of the ULI.

- Prepare the computer for data collection by opening “Exp 06 Shielding” from the Nuclear Radiation w Computers experiment files of Logger Pro. One graph is displayed: count rate vs. layers. The vertical axis is scaled from 0 to 1000 counts/interval. The horizontal axis is distance scaled from 0 to 10 layers. You may need up to 12 layers to stop all of the beta partricles

- Confirm that the source and monitor are positioned so they will not move, and so that there is enough space between them for fifteen layers of aluminum. Remove all aluminum from between the source and monitor.

- Click  to begin collecting data. Logger Pro will begin counting the number of beta particles that strike the detector during each 50-second count interval.

- After at least 50 seconds have elapsed, click the  button. In the entry field that appears, enter 0, which is the number of layers of aluminum. Complete your entry by pressing enter on the keyboard. Data collection will now pause for you to adjust the apparatus.

- Insert one layer of aluminum between the source and detector. Be sure that the aluminum completely covers the source’s “view” of the Geiger tube in the detector. Click  to collect more data, and wait 50 seconds.

- Click , and enter the new number of layers, 1.

- In the same way as before, add a layer of aluminum without moving the source or monitor, wait 50 seconds, and click . Enter the number of layers of aluminum. Click  to resume data collection. Repeat this process until you have completed data collection for ten layers.

- Click  instead of  to end data collection.

data table

| Model equation |  |
| --- | --- |
| Fitted equation with parameters |  |

Analysis

- Inspect your graph. Does the count rate appear to follow your model?

- Fit an appropriate function to your data. To choose a function, look for one that has the same mathematical form as your model. To see the functions available, single-click on the graph. Click the curve-fit button . (Hint: Which fit functions have an x, the horizontal axis variable, in the same special location as in your model equation?) Select an equation from the equation list, and then click . A best-fit curve will be displayed on the graph. If your data follow the selected relationship, the curve should closely match the data. If the curve does not match well, try a different fit and click  again. When you are satisfied with the fit, click .

- Print or sketch your graph. Record the fitted equation and parameters in your data table.

- From the evidence presented in your graph, does the transmission of beta radiation through aluminum match that predicted by your model?

- From the parameters of your fitted equation, determine the fraction f of beta rays transmitted, on average, by one layer of aluminum. Do not use your raw data to calculate the fraction, but instead use the information from your fitted equation. Hint: Remember that A(Bx) = (AB)x.

- A useful approximately of the energy loss by ionization verses thickness of material  (Bethe-Bloch equation) is (-dE/dx)= (0.2 MeV*m2 /kg)( where  ( is the density of the material in kg/m3. Density of Al is 2700 kg/ m3 . Calculate the mean energy of the beta decay by determining the mean energy lost by the particles in the different layers of Aluminum.          (-dE)= (0.2 MeV*m2 /kg)(* dx where dx is the thickness of Al in m. Each layer of aluminum has a thickness of .0002678 m. Assume that the average energy of the particles stopped in each layer is half of the difference between layers

- Cosmic rays continue to strike the detector regardless of the absorbing aluminum. Measure the average background counts in one count interval, and correct your data for background radiation. Complete a trial without the beta source and make a corrected column

- Calculate the mean energy of the particles by dividing the total Energy of all stopped particles by the total number of particles with 0 layers.

- Compare to the accepted 0.54 MeV for Sr-90 beta decay.  Explain why your answer is lower than the accepted value (which is should be).  Hint: Ask Pauli or Fermi what they proposed.

- Write the symbolic equation for Beta decay of Sr-90

Number of Cosmic rays/ 50 s interval _______

Mean counts = Total counts - background (cosmic rays)

| Layers of Al | Thickness Al (m) | Mean counts | Particles stopped | Max Energy Loss in layer MeV | Average energy of particle stopped in layer MeV | Total Energy of all stopped particles |
| --- | --- | --- | --- | --- | --- | --- |
| 0 |  |  |  |  |  |  |
| 1 |  |  |  |  |  |  |
| 2 |  |  |  |  |  |  |
| 3 |  |  |  |  |  |  |
| 4 |  |  |  |  |  |  |
| 5 |  |  |  |  |  |  |
| 6 |  |  |  |  |  |  |
| 7 |  |  |  |  |  |  |
| 8 |  |  |  |  |  |  |
| 9 |  |  |  |  |  |  |
| 10 |  |  |  |  |  |  |
| 11 |  |  |  |  |  |  |
| 12 |  |  |  |  |  |  |

Mean Energy of Beta decay calculation and percent error Explain why your answer is lower than the accepted value (which is should be).

| Model equation |  |
| --- | --- |
| Fitted equation with parameters |  |

- Inspect your graph. Does the count rate appear to follow your model?

- From the evidence presented in your graph, does the transmission of beta radiation through aluminum match that predicted by your model?

From the parameters of your fitted equation, determine the fraction f of beta rays transmitted, on average, by one layer of aluminum.

Extensions

- Use a longer counting interval so that you collect at least 2000 counts when no absorbing aluminum is in place. Is the agreement with the model any different? Try a much shorter count interval. How is the resulting graph different? Why?