Experiment  1

Direction  vrs.  Count Rate

Purpose: To determine the dependence of count rate, at a given altitude, on direction ( NSEW)

Equipment:

Portable Cosmic Ray Detector,

compass

Procedure:

- Make sure your detector is level and facing East.

- Record your data in the data table below.

- Repeat your measurement for a total of five times

- Find the average value.

- Rotate your detector to North and repeat steps 2-4

- Rotate your detector to West and repeat steps 2-4

- Rotate your detector to South and repeat steps 2-4

Data table I

| Direction | Trial 1 | 2 | 3 | 4 | 5 | AVE Count rate |
| --- | --- | --- | --- | --- | --- | --- |
| East |  |  |  |  |  |  |
| North |  |  |  |  |  |  |
| West |  |  |  |  |  |  |
| South |  |  |  |  |  |  |

What is the relationship between direction and count rate based on the data you collected?

Make a graph of average count rate vrs direction

Experiment 2

# Count Rate Vrs Angle Up From Horizontal

Purpose

To establish a relationship between count rate and the angle which the detector makes with horizontal. Also, to discover the primary direction of cosmic rays relative to the Earth’s surface.

Equipment

cosmic ray Detector

Procedure

- repeat the steps in experiment 1

- tilt the detector 10 degrees and repeat #1

- tilt the detector 10 more degrees (to 20 degrees) and repeat #1

- tilt the detector 10 more degrees, for every 10 degree increment, all the way to 90 degrees and measure the count rate at each 10 degree increment five times

- find and record all your average values for each angle

- make a graph of count rate vrs angle

- examine your graph and attempt to determine which function connects count rate with angle

Data Table   II

| Angle with horizontal | Trial 1 | 2 | 3 | 4 | 5 | Ave count rate |
| --- | --- | --- | --- | --- | --- | --- |
| 00 |  |  |  |  |  |  |
| 10 |  |  |  |  |  |  |
| 20 |  |  |  |  |  |  |
| 30 |  |  |  |  |  |  |
| 40 |  |  |  |  |  |  |
| 50 |  |  |  |  |  |  |
| 60 |  |  |  |  |  |  |
| 70 |  |  |  |  |  |  |
| 80 |  |  |  |  |  |  |
| 90 |  |  |  |  |  |  |

How does the count rate vary with angle of the detector from  horizontal ?  Use a graphing calculator to find the function.

Do cosmic rays come in from space vertically ?

### Experiment 3

Count Rate Vrs Altitude (Low Altitude)

Purpose

To establish a relationship between altitude and count rate

Equipment

#### the CHICOs Portable Cosmic Ray Detector

a 12 volt power supply (Car cigarette lighter/power source)     means of transportation up in the (low-altitude) mountains

an altimeter

Procedure

- Determine locations in your area that maximize a difference in altitude

- Follow steps in experiment 1 (obtain five values each time you stop)

- Record your count rates and your altitude in the data table for experiment 3.

- Proceed to next location  of altitude gain

- Find all your average values and make a graph of count rate vrs altitude.

Data Table             Experiment 3

| Location and GPS | Altitude according to DG | Trial 1 | 2 | 3 | 4 | 5 | Ave count rare |
| --- | --- | --- | --- | --- | --- | --- | --- |

How does altitude relate to count rate ?

Make a graph of count rate vrs altitude.

Try to decide which function best describes your graph.

### Experiment 4

Count Rate Vrs Altitude (High Altitude)

Purpose

To establish a relationship between altitude and count rate

Equipment

#### the CHICOs Portable Cosmic Ray Detector

a 12 volt power supply (Car cigarette lighter/power source)

means of transportation with a 12v power source, for travel up in the (high-altitude) mountains

an altimeter (A Casio Pathfinder multi-purpose watch will work, also any GPS device which gives altitude is OK, but it’s slower )

Procedure

- Drive your detector to the beach

- Zero out your altimeter

- Follow steps 3-5 in experiment 1

- Record your count rates and your altitude in the following table.

- Proceed up the road to 500 feet of altitude gain

- Do steps 3 and 4, be sure to obtain  at least five values each time you stop.

- Continue up the highway every 500 feet of altitude gain till you get to the highest point you can drive.

- Find all your average values and make a graph of count rate vrs altitude.  If you can get to 10,000 feet, the graph would be more revealing. This means you may have to drive over a  few hundred miles.

Data Table             Experiment 4

| Altitude ( Ft ) | Trial 1 | 2 | 3 | 4 | 5 | Ave |
| --- | --- | --- | --- | --- | --- | --- |
| 0 |  |  |  |  |  |  |
| 500 |  |  |  |  |  |  |
| 1000 |  |  |  |  |  |  |
| 1500 |  |  |  |  |  |  |
| 2000 |  |  |  |  |  |  |
| 2500 |  |  |  |  |  |  |
| 3000 |  |  |  |  |  |  |
| 3500 |  |  |  |  |  |  |
| 4000 |  |  |  |  |  |  |
| 4500 |  |  |  |  |  |  |
| 5000 |  |  |  |  |  |  |
| 5500 |  |  |  |  |  |  |
| 6000 |  |  |  |  |  |  |
| 6500 |  |  |  |  |  |  |
| 7000 |  |  |  |  |  |  |
| 7500 |  |  |  |  |  |  |
| 8000 |  |  |  |  |  |  |
| 8500 |  |  |  |  |  |  |
| 9000 |  |  |  |  |  |  |
| 9500 |  |  |  |  |  |  |
| 10,000 |  |  |  |  |  |  |

#### How does altitude relate to count rate ?

Make a graph of count rate vrs altitude.

Try to find a function which describes the relationship between altitude and count rate.

# Experiment 5:

# Underground

## Equipment:

## Altimeter, meter stick, 5-meter rope, CHICOS Portable Cosmic Ray Detector with portable 12 v dc source and wagon, digital still camera

## Procedure:

## Determine dimensions of the tunnel and the overbearing rock and soil without a geological contour map

  - Place the 5-meter rope vertically along the side of the entrance to the tunnel and take a close ( 10m ) picture of the entrance. Later, from the photo, determine the height of the tunnel entrance with a dividers, using the image of the 5m rope as a measuring unit.

  - Back up 100m or so from the tunnel entrance and take another photo of the tunnel entrance showing the top of the overbearing rock and soil. Measure the actual distance from the tunnel face to where you took the picture.

  - Measure the distance from the tunnel entrance to the middle  of the tunnel to get the length of the tunnel

  - Use the measured dimensions to find the height of the overbearing rock, assuming it is nearly cylindrical in shape

  - Use this assumption and the measured dimensions to create a thickness v count rate curve.

## Determine the count rate v depth into the tunnel data

## a.  record the altitude of the tunnel

## b. measure the count rate out side of the tunnel, repeat 5 times and find the average

c. measure the count rate at the entrance to the tunnel

d. proceed 10 m into the tunnel and find the count rate

e. proceed another 10 m and count again

f. continue to the middle of the tunnel

III.     Proceed to Dr. Walter Gekelman’s plasma Physics lab at UCLA

- Measure count rate at the entrance to the building ( find altitude)

- proceed to basement lab

- measure  count rate at the entrance to the lab

- proceed to the middle of the lab and measure

- proceed to the far end of the lab and measure

- determine the composition of the roof to Walter’s lab

IV. Proceed to as many other tunnels and caves as possible and collect data

- Produce graphs of count rate v thickness. ( thickness profile)

#### Experiment 5:   Underground Detection

## Data Table

| Location ( GPS) |  |
| --- | --- |
| Length of Tunnel |  |
| Initial Count Outside of Tunnel |  |
| Elevation of Tunnel Entrance |  |
| Type of Rock/Soil |  |

| Location | Counts/min 1 | 2 | 3 | 4 | 5 | Average Value | Check |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Entrance |  |  |  |  |  |  |  |
| 10 m |  |  |  |  |  |  |  |
| 20 |  |  |  |  |  |  |  |
| 30 |  |  |  |  |  |  |  |
| 40 |  |  |  |  |  |  |  |
| 50 |  |  |  |  |  |  |  |
| 60 |  |  |  |  |  |  |  |
| 70 |  |  |  |  |  |  |  |
| 80 |  |  |  |  |  |  |  |
| 90 |  |  |  |  |  |  |  |
| 100 |  |  |  |  |  |  |  |

Spin-offs

- Once several sets of data have been accumulated, values an attenuation value can be assigned to each material through which the radiation has passed. Just calculate the difference in depth and divide it into the difference in count rate. Do this for each 10 m increment and find an average.

- Also, you can effectively take a COSMIC RAY IMAGE of the overbearing rock structure in a tunnel, by just continuing to read values all the way to the other end of the tunnel. Take a value every 10 meters all the way from one end to the other. As you pass the minimum value for cosmic rays( the maximum attenuation) you will eventually re-acquire some value which will begin to increase as the rock overhead gets thinner. The resulting  single line series of values, paints a linear slice of the rock structure as cosmic rays see it. This works only in tunnels with two ends through a mountain.